## Slide 1
IoT • OPERATING SYSTEMS • CYBER SECURITY • DBMS
Secure Smart Laboratory
Equipment Management System
A Raspberry Pi based platform for RFID-authenticated, mutex-safe equipment allocation with encrypted audit logging
RFID Auth
Raspberry Pi 4
AES Encrypted Logs
SQLite DBMS
Harinilekha R - CH.SC.U4CYS25011
Nandika Yazhini – CH.SC.U4CYS25021

## Slide 2
Project Objectives
Security & automation, working together
CORE MISSION
To revolutionize laboratory resource management by integrating IoT, OS principles, cybersecurity, and database management into one seamless, secure system.
RFID Authentication
Restrict access to authorized personnel only using secure RFID UID verification.
Smart Resource Allocation
Automate equipment distribution and prevent conflicts using OS-level Mutex and Scheduling.
Encrypted Audit Trails
Maintain tamper-proof logs with AES encryption for comprehensive usage monitoring.
Secure Smart Laboratory Equipment Management System
2

## Slide 3
System Components
Hardware organized by function, plus the software stack that ties it together
Core Processing
Raspberry Pi 4 — the central brain
RC522 RFID Reader — user ID module
RFID Tags/Cards — unique UIDs
Security Actuators
Servo Motor — electronic lock
Buzzer — unauthorized-access alert
User Interface
16×2 LCD with I2C — status display
LED Indicators — green / red feedback
Infrastructure
Breadboard & jumper wires
Power adapter — stable 5V/3A supply
SOFTWARE
Raspberry Pi OS (Linux)
Python
SQLite Database
VS Code / Thonny IDE
Git (version control)
SUBJECTS INTEGRATED
IoT · Operating Systems · Cyber Security · DBMS
Secure Smart Laboratory Equipment Management System
3

## Slide 4
Operating System Concepts in Action
Every equipment request is handled like a classic OS resource-management problem
Process Management
PROJECT APPLICATION
Each RFID request is treated as an incoming process handled by the Pi.
Process Scheduling
PROJECT APPLICATION
Requests are scheduled and serviced in a defined, fair order.
Mutual Exclusion
PROJECT APPLICATION
A mutex lock ensures only one student can hold a given item at a time.
Resource Allocation
PROJECT APPLICATION
Equipment is allocated only when free — mirrors OS resource management.
Synchronization
PROJECT APPLICATION
Allocation, DB update, and locking stay consistent under concurrent access.
Queue Scheduling
PROJECT APPLICATION
Students wait in a FIFO queue when equipment is unavailable.
Interrupt Handling
PROJECT APPLICATION
Unauthorized scans trigger an immediate buzzer/LED interrupt response.
RESULT
Safe, conflict-free equipment sharing among many students, using proven OS fundamentals.
Secure Smart Laboratory Equipment Management System
4

## Slide 5
Raspberry Pi (Linux)
Servo Lock
LCD
Buzzer+LED
1
USER LAYER
Student Scans RFID Card — Card UID is sent to the Pi as a new access request.
2
PROCESSING LAYER
Raspberry Pi (Linux OS) — Validates the UID against the student database.
3
DATA LAYER
SQLite DB stores every record · AES Encryption seals each log entry so it cannot be altered.
4
ACTION LAYER
Servo unlocks the item · LCD shows the equipment number · Buzzer/LED alert on denied access.
Between Processing and Data: Scheduling, Mutex & Resource Allocation run inside the Pi (see previous slide).
Secure Smart Laboratory Equipment Management System
5

## Slide 6
Methodology: The Smart Workflow
Each step shows the component responsible and exactly what it does
1
Identification
Component: RC522 RFID Reader
Student scans their RFID card at the reader; the system captures the unique UID.
2
Authentication
Component: Raspberry Pi + SQLite
The Pi verifies the UID against the database to confirm identity and permissions.
3
Validation
Component: SQLite Database
Checks equipment availability. If occupied, the student joins the FCFS queue.
4
Allocation
Component: OS Mutex Lock
Applies mutex to prevent double allocation, updates the DB, and encrypts the log.
5
Physical Access
Component: Servo Motor + LCD
Servo unlocks the equipment station; LCD displays the specific equipment ID.
6
Completion
Component: Queue Manager
On return, the system updates status and automatically notifies the next student.
Secure Smart Laboratory Equipment Management System
6

## Slide 7
Demo Scenario
Real-world application — three situations the system must handle correctly
SUCCESSFUL ACCESS
1
Student A scans RFID card.
2
System verifies UID and checks availability.
3
Mutex applied; servo unlocks equipment.
RESULT: Access Granted & Logged
CONFLICT HANDLING
1
Student B requests occupied oscilloscope.
2
System adds Student B to the FCFS queue.
3
Auto-allocated when Student A returns item.
RESULT: Fair Resource Sharing
SECURITY BREACH
1
Unauthorized RFID card is scanned.
2
Red LED flashes and buzzer activates.
3
Event logged in the AES-encrypted database.
RESULT: Access Denied & Alerted
Secure Smart Laboratory Equipment Management System
7

## Slide 8
Thank You
RFID Auth
Raspberry Pi 4
AES Encrypted Logs
SQLite DBMS